## Slide 1: Classification of EEG Signals for Predicting Epileptic Seizures
Alba Asllanaj, Mostafa Shuva
University of Michigan – Dearborn
July 29, 2018

## Slide 2: Agenda
Introduction
Experimental Evaluation
  Algorithms
    Naive Bayes’
    Logistic Regression & Elastic Net
    Support Vector Machine
  Pre-processing Methods
    Fast Fourier Transform (FFT)
    Empirical Mode Decomposition (EMD)
    Continuous Wavelet Transform (CWT)
Results and Analysis
  Experiment 1 - FFT
  Experiment 2 - EMD
  Experiment 3 - CWT
Future Works
Conclusion

## Slide 3: Introduction
Purpose: To predict and classify whether a patient is having an epileptic seizure based on given data
Execution: Use pattern recognition methods based on ECE 5831 studies
Dataset used: UCI
  4097 data points that were recorded from 500 individuals
  Data collected in the time span of 23.5 seconds
    sampled at 173.61 Hz
    each second contains 178 data points
    response variable y is the output of the input vector containing 178 data points for one second
Three major algorithms and three pre-processing methods used

## Slide 4: Experimental Evaluation - Algorithms
Naive Bayes’
  Simple
  Fast
  Benchmark
Logistic Regression & Elastic Net
  Applies L1 & L2 regularization techniques
  Exploits sparsity of the frequency spectrum of EEG data
Support Vector Machine
  Complex
  Requires hyperparameter tuning
  Computationally expensive

## Slide 5: Experimental Evaluation - Preprocessing Methods
Fast Fourier Transform
  Compute the frequency spectrum of the EEG data
Empirical Mode Decomposition
  Extract the intrinsic mode functions of the EEG data
Wavelet transform
  Compute the wavelet filter bank for the EEG data

## Slide 6: Results & Analysis - Performance Metrics
Test and Train Error - accuracy measurement
Sensitivity - the percentage of positive classifications out of patients that had seizures
Specificity - the percentage of negative classifications out of patients that didn’t have seizures
Precision - the percentage of positive classifications classified correctly
Fall out - this is the inverse of specificity
Runtime - how long it took the algorithm to run

## Slide 7: Results & Analysis - Experiment 1
Fast Fourier Transform (FFT)
Comparison of the Fourier transform of the first 3 sample seizure and seizure free EEG signals
The same axes were used to provide an easy visual comparison of the difference between FFT amplitudes
The spectrum seems to be relatively sparse

## Slide 8: Results & Analysis - Experiment 1
Computed the FFT of each of EEG sample
SVM proved to be most accurate with the shortest runtime (tuned algorithm)
  Naive Bayes had similar performance
Logistic Regression had the worst performance
  Lower accuracy with L2 regularization
  Longest runtime when using Elastic Net classifier
Preprocessing: Fast Fourier Transform |  | Based on Test Set |  |  |  |  |  | 
Algorithm | Training Error | Test Error | Sensitivity Score | Specificity Score | Precision | Fall Out | F1 Score | Runtime
Naive Bayes' | 0.0231 | 0.0304 | 0.9815 | 0.9589 | 0.9551 | 0.0411 | 0.9681 | 0.685
Logistic Regression w/ alpha = 0.5 (L2) | 0.4927 | 0.5293 | 1 | 0 | 0.4707 | 1 | 0.6401 | 1.049
Elastic Net w/ alpha = 0.5 (L1) | 0.0111 | 0.0163 | 1 | 0.9692 | 0.9695 | 0.0308 | 0.983 | 2.546
Elastic Net w/ varying alpha we find alpha = 0.01 (L1) | 0.0079 | 0.0098 | 1 | 0.9815 | 0.9796 | 0.0185 | 0.9897 | 8.396
SVM w/ C = 1, gamma = 1, rbf kernel | 0 | 0.5293 | 1 | 0 | 0.4707 | 1 | 0.6401 | 1.832
SVM optimal search with C=0.001, gamma = 109.9486, linear kernel | 0.0014 | 0.0043 | 0.9954 | 0.9959 | 0.9954 | 0.0041 | 0.9954 | 0.675

## Slide 9: Results & Analysis - Experiment 1 SVM Sample

## Slide 10: Results & Analysis - Experiment 2
Empirical Mode Decomposition (EMD)
Used to decompose and simplify complicated signals into a finite number of intrinsic mode functions required to perform signal analysis
Inputs to the classifiers:
  Signal decomposed into intrinsic mode functions
    Returned as a matrix table
  Sum of highest and lowest mode functions

## Slide 11: Results & Analysis - Experiment 2
In comparison to Experiment 1 EMD does not provide a sparse representation of the EEG data
The logistic regression & elastic net’s performance is degraded
Naive Bayes’ and SVM (once its parameters are tuned) perform exceptionally well compared to Logistic Regression
Preprocessing: Empirical Mode Decomposition |  | Based on Test Set |  |  |  |  |  | 
Algorithm | Training Error | Test Error | Sensitivity Score | Specificity Score | Precision | Fall Out | F1 Score | Runtime
Naive Bayes' | 0.0144 | 0.0207 | 0.9931 | 0.9671 | 0.9641 | 0.0329 | 0.9784 | 0.533
Logistic Regression w/ alpha = 0.5 (L2) | 0.5361 | 0.5272 | 0.5242 | 0.4271 | 0.4486 | 0.5729 | 0.4835 | 0.623
Elastic Net w/ alpha = 0.5 (L1) | 0.2804 | 0.2902 | 0.9746 | 0.4743 | 0.6224 | 0.5257 | 0.7597 | 1.043
Elastic Net w/ varying alpha we find alpha = 0.01 (L1) | 0.2804 | 0.2902 | 0.9746 | 0.4743 | 0.6224 | 0.5257 | 0.7597 | 1.043
SVM w/ C = 1, gamma = 1, rbf kernel | 0 | 0.5293 | 1 | 0 | 0.4707 | 1 | 0.6401 | 1.864
SVM optimal search w/ C=155.7453, gamma = 317.992, linear kernel | 0 | 0.038 | 0.9307 | 0.9897 | 0.9877 | 0.0103 | 0.9584 | 1.212

## Slide 12: Results & Analysis - Experiment 3
Wavelet Transform
Localized in time and frequency
Able to determine what frequencies are present, where, and at what scale
CWT was used as the pre-processing method
EWT Decomposition of Interictal EEG
EWT Decomposition of Ictal EEG

## Slide 13: Results & Analysis - Experiment 3
Performance similar to Experiment 1
  Naive Bayes (6.52%) and SVM (6.85%) test error
Logistic regression classifier (with L2 regularization), and untuned SVM classifier perform the worst in accuracy
L1 regularization with elastic net classifier shows immediate performance increase
  CWT behaves similarly to the FFT where it decomposes the EEG signal into its’ frequency representation
Preprocessing: Wavelet Transform |  | Based on Test Set |  |  |  |  |  | 
Algorithm | Training Error | Test Error | Sensitivity Score | Specificity Score | Precision | Fall Out | F1 Score | Runtime
Naive Bayes' | 0.075 | 0.0652 | 0.9792 | 0.8953 | 0.8926 | 0.1047 | 0.9339 | 0.536
Logistic Regression w/ alpha = 0.5 (L2) | 0.4927 | 0.5293 | 1 | 0 | 0.4707 | 1 | 0.6401 | 0.635
Elastic Net w/ alpha = 0.5 (L1) | 0.0739 | 0.0685 | 0.9769 | 0.8912 | 0.8887 | 0.1088 | 0.9307 | 7.11
Elastic Net w/ varying alpha we find alpha = 0.01 (L1) | 0.0712 | 0.0625 | 0.9746 | 0.8994 | 0.896 | 0.1006 | 0.9336 | 6.897
SVM w/ C = 1, gamma = 1, rbf kernel | 0 | 0.5293 | 1 | 0 | 0.4707 | 0 | 0.6401 | 2.245
SVM optimal search w/ C=0.001, gamma = 6.2014, linear kernel | 0.0666 | 0.0685 | 0.963 | 0.9035 | 0.8987 | 0.0963 | 0.9298 | 0.761

## Slide 14: Conclusion
The overall goal for this project is to develop an algorithm SVM, Naive Bayes, and logistic regression as classifiers to determine whether a patient will have a seizure based on the EEG data
We found that:
  Naive Bayes’ performs well for being a simple algorithm
  SVM classifiers perform best when hyperparameters are tuned
  Logistic regression is an excellent choice of classifier for this problem if L1 regularization is used
Future work:
  Better pre-processing techniques
  Neural Networks & Multilayer Perceptrons